## Slide 1: HOUSING FOR DAIRY CATTLE a)Selection of site for Dairy Farm 1. Topography and drainage 2. Soil type 3. Exposure to the sun and protection from wind 4. Accessibility 5. Durability and attractiveness 6. Water supply 7. Surroundings 8. Labour 9. Marketing 10. Electricity 11. Facilities, labour, food

## Slide 2
Type of animal | Covered area | Open area | No.of pens
Buffaloes | 4.0m2 | 8.0m2 | 50/pen
Cattle | 3.5m2 | 7.0m2 | 50/pen
Calves | 12.0m2 | 12.0m2 | 1/pen
Floor space requirements for cattle and buffalo shed
Breed | Feeding space | Watering space
Buffaloes | 75cm/animal | 75cm/animal
Cattle | 75cm/animal | 75cm/animal
Feeding and Watering space requirements

## Slide 3: Main building in dairy farm milk Animal Shed Milking barn or parlour Down calver shed / calving pen Calf pen Young stock or heifer shed Dry animal shed Bull shed Isolation shed Quarantine shed

## Slide 4: milk Animal Shed Essentials of Feeding passage Feeding passage Manger Standing space Gutter or drainage channel Milking passage

## Slide 5: Single row system Double row system

## Slide 6
Tail to Tail System
Advantages

## Slide 7
Face to face system
Advantages and disadvantages

## Slide 10: Milking barn or parlour: Dimensions of Milking barn : Length of standing space : 1.5 – 1.7 m Width of standing space : 1.05 – 1.2m (80% of length, of standing space) Width of central passage : 1.5 – 1.8 m Width of feed alley : 0.75 m Width of gutter : 0.30 m Overhang : 0.75 m Down calver shed/ calving pen:

## Slide 11
Calf pen

## Slide 12: Young stock/ heifer shed: Dry animal shed: Bull shed : Isolation shed: Quarantine shed:
Accessory buildings
a. Store room:
b. b. Milk room:
c. Hay or straw shed:

## Slide 15: Advantages Disadvantages b. Conventional Barns or Stanchion Barns